## Slide 1: JUSTIFICATION AND OPTIMIZATION: International standards and IAEA activities
Jenia Vassileva, Ph.D. Radiation Protection Specialist Radiation Protection of Patients Unit Division of Radiation, Transport and Waste Safety

## Slide 2: International Atomic Energy Agency - IAEA
Member of the United Nations family
Set up as the world´s "Atoms for Peace" organization in 1957
The world´s centre of cooperation in the nuclear field
Winner of Nobel Peace Prize in 2005
Headquarters in Vienna, Austria
164 Member States
2500 staff from > 100 countries
Notes: The IAEA Secretariat is made up of a team of some 2500 multi-disciplinary professional and support staff from more than 125 countries. They come from scientific, technical, managerial, and professional disciplines.
The Agency works with its Member States and multiple partners worldwide to promote safe, secure and peaceful nuclear technologies.

## Slide 3: International Atomic Energy Agency - IAEA
IAEA statute: “To establish or adopt … standards of safety for protection of health and minimization of danger to life … and to provide for the application of these standards”

## Slide 4: IAEA Organizational chart
Director General Mr. Yukija Amano
Department of Technical Cooperation
Department of Nuclear Energy
Department of Management
Department of Nuclear Science and Applications
Programme Support and Coordination
Africa
Asia and Pacific
Europe
Latin America
Department of Nuclear Safety and Security
Radiation, Transport and Waste Safety
Human Health
Department of Safeguards
Director’s offices
Programme of Action for Cancer Therapy
Radiation and Monitoring Section
Radiation Protection of Patient Unit

## Slide 5: IAEA is the focal point for all issues related to radiation protection in medicine
Diagnostic and interventional radiology
Nuclear medicine
Radiotherapy
Notes:   The International Atomic Energy Agency (IAEA) serves as a focal point for all issues related to the radiation protection of patients, staff and the public on medical uses of ionising radiation globally.

## Slide 6: Outline
Overview
Background and current issues
International Basic Safety Standards (BSS)
  Responsibilities for medical exposure
  Justification and optimization
IAEA activities on implementation of BSS

## Slide 7: 1. Background and current issues

## Slide 8: Benefits of the use of radiation in medicine
The use of radiation in medicine has brought tremendous benefits to the global population
Notes: Since the discovery of X-rays and radioactivity the use of radiation in medicine has brought tremendous benefits to the global population

## Slide 9: Benefits of the use of radiation in medicine
More can be done with radiation in medicine
  More equipment
  More complex equipment
  New technologies and techniques
  New role
  Multi-Detector / Dual energy CT
  Digital Radiography
  Hybrid imaging
  Image-guided interventional procedures
  PACS, RIS
  Tomosynthesis, Cone beam CT
  IMRT, IGRT in radiotherapy……
Notes: Since the discovery of X-rays and radioactivity the use of radiation in medicine has brought tremendous benefits to the global population

## Slide 10: Benefits of the use of radiation in medicine
Global increase of the use of radiation
Access vary around the world
Issues vary around the world
Tailored approaches needed
Notes: Since the discovery of X-rays and radioactivity the use of radiation in medicine has brought tremendous benefits to the global population

## Slide 11: Global trends
Growth of high-dose radiation procedures: CT, interventional , SPECT-CT, PET-CT
A significant fraction (20-50% in some areas) of radiological examination may be medically inappropriate
Increased individual patient doses from diagnostic exams
  Over the 22 years study period, 32000 patients
  > 33% of patients underwent more than 5 lifetime CT scans
  5% underwent 22-132 CT scans
  15% received doses over 100 mSv;
  5% received doses over 250 mSv
  Increased cancerogenic risk at these doses
Sodickson et al. Radiology 251; 175-184, 2009

## Slide 12: Radiosensitivity in children: three large scale studies
There is a small but definite risk of a CT scan performed in childhood to be associated with a later risk of cancer as a consequence of the CT examinations
Notes: Additionally, three recent large-scale epidemiological studies provide evidences that there is a small but definite risk of a CT scan performed in childhood to be associated with a later risk of cancer as a consequence of the CT examinations

## Slide 13: Medical radiation can cause harm
  Reports of accidents in radiotherapy, leading to injuries and death
Radiation accidents involving medical uses have accounted for more acute radiation deaths than any other source, including Chernobyl
Notes: Hundreds of radiotherapy patients have been affected by accidental exposure because of improper calibration or improper use of radiotherapy equipment, or due to the inadequate knowledge or lack of awareness among the medical staff.
Radiation accidents involving medical uses have accounted for more acute radiation deaths than any other source, including Chernobyl
These accidents do not only affect patients directly (e.g. harm and death), but might also undermine the public’s confidence in the treatment
Preventable medical errors overall also cost countries billions of dollars each year

## Slide 14: Medical radiation can cause harm
Computed tomography
Interventional radiology
Rarely in diagnostic radiology:
  1 case per 10000 patients;
In complex interventional procedures
CAN BE AVOIDED (dose treshold for tissue reactions)
Notes: Skin injuries or hair loss have been observed in fluoroscopically guided interventional procedures and even in computed tomography, with the same reasons identified – equipment failures and human errors due to neglecting the radiation risk and lack of adequate radiation protection system.

## Slide 15: Medical radiation can cause harm
Human errors (improper calibration or improper use)
Lack of knowledge or experience
Lack of resources, support or safety culture
Lack of awareness

## Slide 16: Patient dose and individual risk vary greatly
0.01mSv
0.1mSv
1mSv
10 mSv
Radiography
CT, NM, Image guided interventional procedures
Skin doses –
Image guided interventional procedures
Radiation therapy, mainly to the target volume
Annual dose from natural background
Increased risk of cancer
Tissue reactions (skin, eye lens,..)
100 mSv
1 000 mSv
10 000 mSv
100 000 mSv
Lethal whole body dose
Radiological procedures
Radiation risk

## Slide 17: Do more good than harm
Radiation can cause harm
Radiation saves lives
Short-term effects (deterministic)
Long-term effects (stochastic)
  Carcinogenesis
  Hereditary effects
  Effects in the embryo/foetus
Principles of radiation protection
  Dose limits don’t apply to medical exposures
  Justification - perform only appropriate procedures
  Optimization - perform procedure appropriately
Notes: Medical uses of ionizing radiation are amongst the longest established applications of ionizing radiation, and one of the most rapidly developing areas. The medical benefits of the use of ionizing radiation are indisputable, but there is an associated radiation risk for patients and medical staff. Patient and staff doses vary in a large extend, and both deterministic and stochastic effects are possible and have been observed.
Hundreds of radiotherapy patients have been affected by accidental exposure because of improper calibration or improper use of radiotherapy equipment, or due to the inadequate knowledge or lack of awareness among the medical staff. Skin injuries or hair loss have been observed in fluoroscopically guided interventional procedures and even in computed tomography, with the same reasons identified – equipment failures and human errors due to neglecting the radiation risk and lack of adequate radiation protection system. However, the increased utilization of image guided procedures and their use with a little concern of radiation risk, lead to observation of high doses to the eye lens of interventionists, and as a consequence – increased risk of radiation-induced cataract. Additionally, three recent large-scale epidemiological studies provide evidences that there is a small but definite risk of a CT scan performed in childhood to be associated with a later risk of cancer as a consequence of the CT examinations
Therefore, systematic approach should be applied to ensure that a balance is in place between being able to utilize the benefits from medical uses of ionizing radiation and minimizing the risk of radiation effects to patients, workers and members of the public.

## Slide 18: 2. International Basic Safety Standards (BSS)

## Slide 19: IAEA Safety Standards hierarchy
Safety Guides
Safety Requirements
Safety Fundamentals
All Safety Standards go through the IAEA Safety Standards Committees and Commission, and receive formal Member State comments
Fundamental safety objectives and principles for protecting people and environment moral obligation
Requirements that must be met to ensure protection of people and environment legal obligations, "shall"
Recommended ways of meeting the requirements, “should”

## Slide 20: International BSS
Not mandatory
  No obligation for States to bring legislation into conformity, etc.
However
  Mandatory for Member States receiving technical assistance from IAEA
  Used as a template for many national regulations
Published July 2014
Co-sponsors:

## Slide 21: International BSS
Effects of radiation
Recommendations for protection
Essential principles
(moral obligation)
Essential requirements
(legal obligation)
Notes: The jointly sponsored edition of the Safety Requirements “Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards” was published as General Safety Requirements Part 3 in July 2014. This edition supersedes the Interim Edition that was published in 2011, which itself superseded the International Basic Safety Standards that were issued as IAEA Safety Series No. 115 in February 1996. The joint sponsors are EC, FAO, IAEA, ILO, OECD/NEA, PAHO, UNEP, and WHO. The BSS will be published in all the official languages of the IAEA in due course.

## Slide 22: International system of radiation protection
Principles:
- Justification
- Optimisation
- Dose limitation
Categories of exposure
- Medical
- Occupational
- Public
Requisites
- Information
- Assessment of exposure
- Stakeholders involvement
Dose criteria
- Dose limits
- Dose constraints
- Reference levels
Exposure situations
- Planned
- Emergency
- Existing

## Slide 23: BSS definitions
Medical radiation facilities A medical facility where radiological procedures are performed
  Diagnostic radiology
  Image guided interventional procedures
  Nuclear medicine
  Radiation therapy

## Slide 24: BSS definitions
Medical exposure:
Exposure incurred by:
Patients* for the purpose of medical or dental diagnosis or treatment
Carers and comforters **
Volunteers in a programme of biomedical research involving their exposure
*A patient is an individual who is a recipient of services of health care professionals and/or their agents that are directed at (a) promotion of health; (b) prevention of illness and injury; (c) monitoring of health; (d) maintaining health; and (e) medical treatment of diseases, disorders and injuries in order to achieve a cure or, failing that, optimum comfort and function. Some asymptomatic individuals are included.
For the IAEA safety standards, the term ‘patient’ refers only to those individuals undergoing radiological procedures.
**Carers and comforters are persons who willingly and voluntarily help (other than in their occupation) in the care, support and comfort of patients undergoing radiological procedures for medical diagnosis or medical treatment

## Slide 25: Medical exposure in the BSS
Responsibilities (Req. 34 – 36)
Justification (Req. 37)
Optimization (Req. 38)
Pregnant or breast-feeding female patients (Req. 39)
Release of patient after radionuclide therapy (Req. 40)
Unintended and accidental medical exposure (Req. 41)
Reviews and records (Req. 42)

## Slide 26: Responsibilities
Government (Req. 2 and 34):
Establish a legal and regulatory framework
Ensure, as a result of consultation between Health Authorities, professional bodies and the Regulatory Body, establishment of:
    Diagnostic reference levels (DRLs) (for patients)
    Dose constraints are established (for carers and comforters and volunteers in biomedical research)
    Guidelines and criteria for the release of patients after radionuclide therapy
Regulatory Body (Req. 3 and 35):
Establish and adopt regulations and guides for protection and safety
Establish a system to ensure their implementation
Authorization of health professionals to take the responsibilities of the Standards (only if they are specialized in the appropriate area; meet the respective education, training and competence requirements; are named in a list maintained up to date by the registrant or licensee)
Notes: An area identified in the review of the BSS as needing improvement.

## Slide 27: Responsibilities
Registrants and licensees (Req. 4 and 36):
Have the prime responsibility for protection and safety, which cannot be delegated
Ensure that no person incurs a medical exposure unless:
      it is a radiological procedure that has been requested by a referring medical practitioner and information on the clinical context has been provided, or it is part of an approved health screening programme;
      the medical exposure has been justified;
      a radiological medical practitioner has assumed responsibility for ensuring protection and safety in the planning and delivery of the medical exposure,
      the person subject to exposure has been informed as appropriate of the expected benefits and risks.
    Ensure that sufficient medical and paramedical personnel are available

## Slide 28: Health professionals
  Medical radiation technologist
  Medical physicist
  Radiophar-macist
  Radiological medical practitioner
  Competence is normally assessed by the State by having a formal mechanism for registration, accreditation or certification
  Referring medical practitioner

## Slide 29: International BSS – justification and optimization

## Slide 30: Justification and optimization
Justification
Optimization
Perform only appropriate procedure
Perform procedure appropriately

## Slide 31: Justification of medical exposures
3 levels of justification according to the ICRP
Level | Scope | Responsibility
Level 1 | General justification of the use of radiation in medicine | Taken for granted – accepted as doing more good than harm
Level 2 | Generic justification of a given radiological procedure | Health authority in conjunction with appropriate professional bodies
Level 3 | Justification of medical exposure for individual patient | Consultation between the radiological medical practitioner, and the referring medical practitioner

## Slide 32: Justification for an individual patient
What needs to be considered?
  Appropriateness of the request
  Urgency of the procedure
  Characteristics of the exposure
  Characteristics of the individual patient
  Relevant information from previous radiological procedures
    Clinical context, medical history
    Knowledge about procedure – benefits, risks, limitations
  Referring medical practitioner
  Radiological medical practitioner
    “Request for consultation” rather than “order/instruction to perform”
Notes: The justification of medical exposure for an individual patient shall be carried out by means of consultation between the radiological medical practitioner and the referring medical practitioner, as appropriate, with account taken, in particular for patients who are pregnant or breast-feeding or are paediatric, of:
(a) The appropriateness of the request;
(b) The urgency of the radiological procedure;
(c) The characteristics of the medical exposure;
(d) The characteristics of the individual patient;
(e) Relevant information from the patient’s previous radiological procedures.

## Slide 33: Justification for an individual patient
    Clinical context, medical history
    Knowledge about procedure – benefits, risks, limitations
  Referring medical practitioner
  Radiological medical practitioner
    “Request for consultation” rather than “order/instruction to perform”
  Relevant national or international referral guidelines to be taken into account for the justification of the medical exposure of an individual patient
  Particular attention to be taken for patients who are pregnant, breast-feeding or paediatric
Notes: The justification of medical exposure for an individual patient shall be carried out by means of consultation between the radiological medical practitioner and the referring medical practitioner, as appropriate, with account taken, in particular for patients who are pregnant or breast-feeding or are paediatric, of:
(a) The appropriateness of the request;
(b) The urgency of the radiological procedure;
(c) The characteristics of the medical exposure;
(d) The characteristics of the individual patient;
(e) Relevant information from the patient’s previous radiological procedures.

## Slide 34: Asymptomatic individuals – intended early detection of disease
  Health screening programme – justification to be performed by the health authority in conjunction with appropriate professional bodies
  If not as part of an approved health screening programme – individual justification by:
    Referring medical practitioner and radiological medical practitioner
    In accordance with professional body guidelines
    Individual informed of the benefits, risks and limitations
Notes: Justification for radiological procedures to be performed as part of a health screening programme for asymptomatic populations shall be carried out by the health authority in conjunction with appropriate professional bodies.
Any radiological procedure on an asymptomatic individual that is intended to be performed for the early detection of disease, but not as part of an approved health screening programme, shall require specific justification for that individual by the radiological medical practitioner and the referring medical practitioner, in accordance with the guidelines of relevant professional bodies or the health authority. As part of this process, the individual shall be informed in advance of the expected benefits, risks and limitations of the radiological procedure.

## Slide 35: Volunteers as part of a programme of biomedical research
Justified only if:
  it is in accordance with the provisions of the Helsinki Declaration
  takes into account the guidelines published by the Council for International Organizations of Medical Sciences, together with the recommendations of the ICRP;
Subject to approval by an ethics committee (or other institutional body with similar functions)
Subject to dose constraints
Subject to applicable national / local regulations
Notes: 3.161. The medical exposure of volunteers as part of a programme of biomedical research is deemed to be not justified unless:
(a) It is in accordance with the provisions of the Helsinki Declaration [20] and takes into account the guidelines published by the Council for International Organizations of Medical Sciences [21], together with the recommendations of the ICRP [22];
(b) It is subject to approval by an ethics committee (or other institutional body that has been assigned functions similar to those of an ethics committee by the relevant authority), subject to any dose constraints that may be specified (as required in paras 3.149(a)(ii) and 3.174), and subject to applicable national regulations and local regulations.

## Slide 36: Optimization of protection and safety
Req. 38: Registrants and licensees and radiological medical practitioners shall ensure that protection and safety is optimized for each medical exposure.
Too low a radiation dose could be as bad as too high a radiation dose
It is of paramount importance that the medical exposure leads to the required outcome.
Diagnostic quality
Patient dose

## Slide 37: Optimization of protection and safety
Diagnostic quality
Patient dose
  Design considerations for equipment
  Operational considerations
  Calibration
  Dosimetry of patients
  Diagnostic Reference Levels (DRLs)
  Quality Assurance
  Dose constraints

## Slide 38: Optimization cycle
1. Asses typical dose in a X-ray room
2. Compare with national DRL
3. Image quality adequate?
4. Apply changes
DRLs
Facility 1
Facility 2
Facility 3
Facility 4
Facility 5
Facility 6

## Slide 39: Optimization of protection and safety
Particular aspects of medical exposures are considered in the optimization process for:
Paediatric patients
  Embryo or fetus
  Breastfed infant (from procedure with radiopharmacetical performed to mother)

## Slide 40: Optimization of protection and safety
Arrangements for appropriate radiation protection in cases where a female patient is or might be pregnant or is breast-feeding.
signs in appropriate languages in appropriate places;
other means of communication, to request female patients who are to undergo a radiological procedure to notify in the event that she is or might be pregnant, or she is breast-feeding
procedures for ascertaining the pregnancy status of a female patient of reproductive capacity before the performance of any radiological procedure that could result in a significant dose to the embryo/fetus.

## Slide 41: Unintended and accidental medical exposures
New requirement aimed at prevention
Scope for investigation by the licensee expanded, to now include:
  For diagnostic or image-guided interventional procedures
    Wrong individual, wrong volume/tissue of the patient
  Inadvertent in utero exposures
Licensee must keep a record
Reporting to Regulatory body limited to significant events or as required by the Regulatory body

## Slide 42: Radiological review
A requirement for radiological review introduced
Radiological review: A systematic examination or review of the radiological procedures being performed in a given medical radiation facility, that seeks to improve the local implementation of the radiation protection principles of justification and optimization.
Responsibility of the radiological medical practitioners

## Slide 43: From standards to practice
Difficulties:
  medical domain
  requires cooperation between regulatory body, health authority, professional bodies
Barriers:
  lack of awareness
  self-referral
  defensive medicine
  self-presentation
  financial, social, or medico-legal pressures
Standards

## Slide 44: 3. IAEA activities on implementation of BSS

## Slide 45: IAEA activities to support implementation
Providing standards
Providing training Providing guidance
Facilitating knowledge exchange
Giving technical assistance
Building awareness
45
Technical documents
Workshops
Reporting systems
Scientific publications
Press campaigns
Information campaigns
Meetings
Public website
Missions
Assessments
Direct advice
Providing tools
Involve in projects
Scientific visits
Fellowships
Training material
Training courses
Safety standards
Safety reports
AAA International campaign
Awareness, Appropriateness, Audit

## Slide 46: Providing guidance – safety guide
Safety Guide on Radiation Protection and Safety in Medical Uses of Ionizing Radiation
  How the BSS applies to facilities
  Aimed at (primarily):
    End-users: Medical radiation facilities: “What do I need to do to ensure that my facility’s medical uses of radiation are in compliance with the BSS”
    Regulatory Bodies: “What do the Government need to do to ensure that the facilities in the country meet the requirements of the BSS”
  The Safety Guide is expected to be co-sponsored by relevant UN organizations (e.g. WHO, PAHO, ILO).
  Cooperation in developing from international / regional organizations

## Slide 47: Providing guidance – safety guide
Development process:
    2012 – 2014: first draft prepared by 3 drafting group (DR&IR; NM; RT)
    2014 – 2015: soliciting and addressing comments by MS, and organizations internal approvals, comments from MS, next draft, approval by a number of committees….
    2015 – 2016: target publication
Safety Guide on Radiation Protection and Safety in Medical Uses of Ionizing Radiation

## Slide 48: Providing guidance – safety reports
IAEA publications on radiation protection of patients
Safety Reports published in last few of years on : (1) PET/CT; (2) Guidance levels in interventional procedures; (3) Cardiac CT; (4) CT Colonography and (5) Release of Patients after Radionuclide Therapy; (6) Radiation Protection in Paediatric Radiology
Freely available from www.iaea.org

## Slide 49: Providing guidance - website
Updated monthly
Information for
Health professionals
Member States
Patients
Additional resources
Publications
Safety Standards
Training material
Posters
Dedicated public website – http//rpop.iaea.org

## Slide 50: Providing guidance – training material
Dedicated public website – http//rpop.iaea.org

## Slide 51: Providing guidance – posters and leaflets
Dedicated public website – http//rpop.iaea.org

## Slide 52: Providing guidance – posters and leaflets

## Slide 53: Facilitating knowledge exchange
Technical meetings
March 2015: Justification of medical exposure
April 2015: Patient exposure tracking
2-6 November 2015: Implementation of the Safety Guide

## Slide 54: Facilitating knowledge exchange
Incident reporting databases
  Anonymous
  Voluntary
  Learning from incidents
SAFRAD
  Interventional procedures
SAFRON
  Radiation therapy

## Slide 55: Facilitating knowledge exchange
Information databases for medical staff
ISEMIR Working Group on Interventional Cardiology
  Gathering an overview picture of the situation concerning occupational exposures and radiation protection of staff in interventional cardiology all over the world
Lens injury studies among medical staff
  RELID (Retrospective Evaluation of Lens Injuries and Dose) (RELID) started in 2008 and covers staff working in interventional cardiology, with e.g. SOLACI: Latin American Society on Interventional Cardiology

## Slide 56: Building awareness
Information campaign for strengthening justification in diagnostic imaging
AAA
                Awareness
                Appropriateness
                Audit

## Slide 57: Building awareness
https://www.facebook.com/rpop.iaea.org
4000 likes in Facebook
1200 likes in Twitter
https://twitter.com/rpop_iaea

## Slide 58: Technical cooperation
Regional and national projects:
  High number of countries participating in technical cooperation projects on radiation protection of patients
  Tasks in all major areas of patient protection
  Expert missions, direct advice and provision of tools
  Fellowships
  Scientific Visits
  Regional and national training courses

## Slide 59: Technical cooperation

## Slide 60: Technical cooperation

## Slide 61: Publications from the TC projects

## Slide 62: Providing training
Providing training courses
  Regional training courses
  National training courses supported
  Main target audience: health professionals in hospitals; but also radiation protection professionals

## Slide 63: International Action Plan for Radiation Protection of Patients
  Bonn Conference
  536 participants and observers in attendance
  77 Member States and 16 organizations represented
  88 presentations in the main programme
  2 breakout sessions (EC and UNSCEAR)
  214 contributed papers
  68 posters displayed

## Slide 64: International Action Plan for Radiation Protection of Patients
The Bonn Call-for-Action
joint position statement with WHO
highlights ten main actions and related sub-actions, that were identified as being essential for the strengthening of radiation protection in medicine over the next decade.
Next IAEA conference on Radiation Protection in Medicine in 2017

## Slide 65: Conclusion
Medical uses of ionizing radiation only have a place in the context of medical practice. The system for ensuring radiation protection needs to fit in with the larger system for ensuring good medical practice
The International BSS set basic requirements for protection and safety
Implementation is a challenging task; reaching stakeholders and making efforts effective and lasting is complex
A systematic approach should be applied to ensure that there is a balance between being able to utilize the benefits from medical uses of ionizing radiation and minimizing the risk of radiation effects to patients, workers and members of the public
The IAEA addresses these issues globally, in co-operation, through the International Action Plan, in a variety of actions
The MS are welcome to contribute and use available resources

## Slide 66
Keep being informed
Visit us at http//rpop.iaea.org
j.vassileva@iaea.org