## Slide 1: JUSTIFICATION AND OPTIMISATION FACTS AND SOLUTIONS
GUY FRIJA
CHAIR,EUROSAFE ALLIANCE
ESR PAST-PRESIDENT
LISBON,SEPT 2015

## Slide 2: REGULATION
2013 : Basic Safety Standards
- Optimisation:ALARA-DRLs
- Justification:Guidelines
- Clinical audits

## Slide 3: CHALLENGE 1: JUSTIFICATION
Radiological examinations should be performed only if they are doing more good than harm (“clinically justified”)
CHALLENGE 1: JUSTIFICATION
DOSE DATAMED 2

## Slide 4
CHALLENGE 1: JUSTIFICATION

## Slide 5
CT
MRI
USA: 30 % of inappropriate tests

## Slide 6
The clinical justification is established through evidence-based Clinical Guidelines
CHALLENGE 1: JUSTIFICATION
European BSS Directive 2013/59/EURATOM
MUST HAVE CIG
MUST USE CDS

## Slide 7: REFERRAL GUIDELINES
European survey by the European Society of Radiology (ESR)
Availability of Referral Guidelines (~ 70%)
Production: UK and France
Adopted and adapted: others
CHALLENGE 1: JUSTIFICATION

## Slide 8
“In Belgium we have referral guidelines; in fact, nobody really takes them into account ”…
“Referral guidelines for diagnostic imaging in general are not in use in Hungary ”…
“They are not used in the Netherlands ”…
“Although we have several official referral guidelines published (in Spain), they are not used generally speaking ”
“In Italy the referral guidelines were published in 2004 by the Ministry of Health. Unfortunately they are not always followed in clinical practice ”…
“There is no official guide line enforcement in the State service in Ireland ”…
“In Germany, the guidelines are note routinely used ”…
“In France, there are guidelines, but they are not used ”…
CHALLENGE 1: JUSTIFICATION

## Slide 9: CHANGE IN PARADIGM
Producing
Guidelines
Using
Guidelines
CHALLENGE 1: JUSTIFICATION

## Slide 10: CHANGE IN PARADIGM
Producing
Guidelines
Using
Guidelines
CHALLENGE 1: JUSTIFICATION
HOW TO PROCEED?

## Slide 11
Justification
Regulation
Incentives
Health Policy
CDS
Culture
Behaviour

## Slide 12: CHANGE IN PARADIGM
CDS
Producing EBM
Using EBM
CHALLENGE 1: JUSTIFICATION

## Slide 13: CDS IN IMAGING
Proven efficiency in the literature
Patient centric, i.e. « personalised »
Adaptable to the practice setting
Scalable : focused or comprehensive

## Slide 14: CONCEPT OF CDS
Answer to a clinical question
Provide guidance based on appropriatness criteria
Integrated in the physician workflow
Ideally integrated into the EMR

## Slide 15: CONCEPT OF CDS
Content is an algorithmic format of pre existing textual guidelines
Technical platform is a sophisticated software which operates according to pre- and post-test probabilities

## Slide 16
CHALLENGE 1: JUSTIFICATION

## Slide 17
Decision support system
Konwledge Base
DataBase
Inference Engine
Timely
CDS/CPOE
Point of Care DS
Referral Guidelines
EHR/HIS/RIS

## Slide 21
Example of ROE form displayed after provider selects MR imaging of the lumbar spine.
Sistrom C L et al. Radiology 2009;251:147-155
©2009 by Radiological Society of North America
Notes: Example of ROE form displayed after provider selects MR imaging of the lumbar spine. DJD = degenerative joint disease, syx = symptoms.

## Slide 22
Screenshot of the DS feedback displayed after submitting a request for MR imaging of the lumbar spine with symptom of “back pain improved with exercise” and abnormal result at previous examination of “abnormal x-ray DJD [degenerative joint disease].” PCP's ...
Sistrom C L et al. Radiology 2009;251:147-155
©2009 by Radiological Society of North America
Notes: Screenshot of the DS feedback displayed after submitting a request for MR imaging of the lumbar spine with symptom of “back pain improved with exercise” and abnormal result at previous examination of “abnormal x-ray DJD [degenerative joint disease].” PCP's = primary care physicians.

## Slide 23: PROVEN CDS BENEFITS
Improve the appropriate use by a significant amount
Decrease the use by a small amount
CHALLENGE 1: JUSTIFICATION

## Slide 24: Massachusetts General Hospital High Cost Imaging
Effects of CDS
2000 - 2007
Quarters 2000-2007
= Ordered with ROE
= Total exams
Adjusted
Annual Compound
Growth Rate
12%
Adjusted
Annual Compound
Growth Rate
1%
Sistrom C L et al. Radiology 2009;251:147-155

## Slide 25: MGH EXPERIENCE
Lessons Learned
  Change Management – CDS is just the tool
  Multidisciplinary Teams - Continual process for evaluation & reassessment
  CDS is as effective as RBMs for managing inappropriate utilization
  When implemented correctly, there is a higher physician acceptance
  Need physician feedback to reduce variability and utilization
Courtesy of K.Dreyer
CHALLENGE 1: JUSTIFICATION

## Slide 26: AMERICAN EXPERIENCE
CHALLENGE 1: JUSTIFICATION
ACR:CONTENT
NDSC:PLATFORM
ACR SELECT

## Slide 27: TRANSATLANTIC PARTNERSHIP
MOU with ACR,and agreement with NDSC
Europeanisation,Pilot studies,Dissemination
ESR i GUIDE

## Slide 28
Brain:7%
Cardiac:28%
Breast:2%
Chest:1%
MSK:4%
Urinary:0%
Women’s:0%
DISCREPANCIES:9%
GI:0.5%
Vascular:7%

## Slide 29: LOCALISATION
A crucial step for adoption by the physicians
Possible to add a new indication which would be reviewed by the ACR/ESR experts
-either remain local
-or incorporated to the general stock
Possible to change the rating of the tests
-Ultrasound for example probably more used in some EU countries than in the USA

## Slide 30: POTENTIAL SITES
  Austria
  Belgium
  Croatia
  Denmark
  France
  Germany
  Hungary
  Ireland
  Italy
  Netherlands
  Norway
  Poland
  Spain
  Sweden
  Switzerland
  United Kingdom

## Slide 31: BARCELONA PILOT PHASE
Independent pilot phase
Translation and coding adaptation without any difficulty
Firstly targeted at GPs : very well received
Next expansion to emergency physicians

## Slide 32: CHALLENGE 2: OPTIMISATION
“Radiological examinations must be performed with a dose relevant to the clinical question which should provide an appropriate image quality”
DRL IMAGE QUALITY
CHALLENGE 2: OPTIMISATION

## Slide 33: CHALLENGE 2: OPTIMISATION
CHALLENGE 2: OPTIMISATION
DOSE DATAMED 2

## Slide 34: DRL
They are not « target doses »
They are not for individuals
They are for a group of patients
They serve to give a figure of the dose distribution for a given examination in a given facility
They are determined by surveys,usually at the national levels and with specific protocols
CHALLENGE 2: OPTIMISATION

## Slide 35: DRL
They reflect a technical protocol and not a clinical indication
Their collection is rather complex and requires radiographers,medical physicists and radiologists cooperation
They are not following the pace of the technological progresses
CHALLENGE 2: OPTIMISATION

## Slide 36: DRL:OPTIONS
Wait and see the National or the European DRLs
Proactive
- Patients are very much worry with the dose practices exposure and need to be reassured
CHALLENGE 2: OPTIMISATION

## Slide 37: DRLs:OPTIONS
Wait and see the National or the European DRLs
Proactive
- It has been established that using DRLs improves the quality of the practices exposures
CHALLENGE 2: OPTIMISATION

## Slide 38
Chart: After dose optimization
CORONARY CALCIFICATION SCORING
Decrease of the mean DLP from 142.6  23.2 mGy.cm to 79.5  15.8
Chart: Before dose optimization

## Slide 39
Chart: DLP (mGy.cm)
 | 579 | 504.3 | 494.8 | 375.1 | 356.2 | 366.5
 | 265 | 228.5 | 202.2 | 187.9 | 186.8 | 208.9
 | 422 | 366.4 | 348.5 | 281.5 | 271.5 | 287.7
2009-2012

## Slide 40
NRDmoy. = 427  157 mGy.cm
NRDréf*. = 500 mGy.cm
Chart: N° patient
2009
CHEST CT

## Slide 41
DLPmax. = 994 mGy.cm
Arms along the body
Notes: Qualité d’image choisie par observateur détermine directement la réduction de dose souhaitée.

## Slide 42: AUTOMATIC DOSE RECORDING
Automatic dose management software (10/15 available)
ACR Dose Index registry:over 800 facilities and 16 million examinations
BENCHMARKING
CERTIFICATION

## Slide 43: EUROSAFE IMAGING SURVEYS
Based on clinical indications:stroke,pulmonary embolism,appendicitis…
Preliminary results are showing a strong heterogeneity in dose exposure

## Slide 44
(*Status: 27 January 2015. As the survey is still open, the data displayed is preliminary.)
PRELIMINARY SURVEY FINDINGS
Head CT for Acute Stroke *

## Slide 45
(*Status: 27 January 2015. As the survey is still open, the data displayed is preliminary.)

## Slide 46
(*Status: 27 January 2015. As the survey is still open, the data displayed is preliminary.)
HOW IS YOUR PRACTICE??

## Slide 47
(*Status: 27 January 2015. As the survey is still open, the data displayed is preliminary.)
AND YOU WILL SEE!!!
BECOME FRIENDS OF EUROSAFE
FILL THE SURVEYS!!

## Slide 48: CHALLENGE 3: EQUIPMENT
Recent CT: huge decrease of the dose
Dose by 50%
CHALLENGE 3: EQUIPMENT

## Slide 49: Action 4: Equipment Update Policy
    ESR paper on renewal of imaging equipment (published October 2014)
      Equipment life cycles are becoming shorter due to rapid technological advances
      Equipment older than 10 years must be replaced to avoid delays in diagnosis and safety problems
      For efficient maintenance and replacement, ESR advocates annually updated 5-year plans

## Slide 50
The ESR Call for a European Action Plan for Medical Imaging
  QUALITY & SAFETY
  - Policy of equipment upgrade
  EDUCATION & TRAINING
  RESEARCH
  E-HEALTH
    - Support use of clinical decision support and referral guidelines
Brussel,2014

## Slide 51
- ESR Patient Advisory Group
- European Commission
- HERCA (radiation protection authorities)
- ESPR (European Society of Paediatric Radiology)
- CIRSE (Cardiovascular and Interventional Radiological Society of Europe)
- EFOMP (European Federation of Organizations for Medical Physics)
- EFRS (European Federation of Radiographer Societies)
- COCIR (European Coordination Committee of the Radiological, Electromedical and Healthcare IT Industry)
Stakeholders
Regulators
Patients
Experts
Industry

## Slide 52: ACTION ITEMS
IAEA-WHO Bonn Call for Action
    1: Justification
    2: Justification
    3: Optimisation and Safety
    4: Optimisation and Safety
    5: Manufacturers’ role
    6: Education
    7: Research
    8: Information
    9: Safety culture
    10: Patient
    11: Globalisation
    EuroSafe Imaging
    1: Clinical Decision Support
    2: Clinical audit
    3: PiDRL project, data collection
    4: Equipment update policy
    5: Cooperation with COCIR (industry)
    6: E-courses, education projects
    7: MELODI (research platform)
    8: Data collection surveys
    9: GPS and KIQSI
    10: Website, ESR newsletters
    11: ESR Patient Advisory Group
    12: Network of campaigns
EUROSAFE

## Slide 53: Thank you for your attention !!!